Notes for troubleshooting the CTC169BU chassis for a P46101WK PTV

Suppliers:

PC Richard Service Center – 1800-696-2000

www.Electronicx.com

www.TriTronicsInc.com - Electronic Parts Express – 1800-217-4889 – Placed order

CTC169BU Chassis:

Power Supply voltages:   (taken in stand-by mode eg: plugged in & off)

+140vdc, +15vdc, +16vdc and –16vdc

Parts List:

RCA#

242907  - use 198596

198596  - CR4401 – May be ‘Pin Diode’ in HOT (horiz. output transtr)		$3.25

243636  - equiv. To 1N5392 - use 169590

169590  - CR4402, CR4118 – Use 1N5404 3A Power Supply Diodes		$3.25

??????  - Q4401 - 2SD1885  HOT						$5.00

205064  - High Voltage Distribution Block -					$69.89

223221  - 4 pieces - Gaskets for HV Dist. Block					$

223222  - 1 piece – Gasket for HV Dist. Block					$

- C4104 – 15uf/100v 105 deg C. – Shutdown Cap on U4101 reg ic	$

- C4??? – 2.2uf/100v 105 deg C. – Stand-by Voltage Cap on U4101	$

- C4145 – 1000uf/35v 105 deg. C. – Filter Cap				$

200165  - U4101 Voltage Regulator IC – TEA-2261				$11.60

??????  - U3200 – EPROM for the P46101 PTV					$15.00

Test Points:

Volts DC

CR4116	140

CR4118	13.6

CR4117	7

CR4119	17

Q4610 Emitter	5

Common caps that go bad on the CTC169 chassis:

C: 4401, 4402, 4105, 4108, 4115, 4141, 4145, 4503, 3124